## Slide 1: Introduction to Bare Bear Metal on MP13
Bear Photo : Byrdyak

## Slide 2: Agenda
#
Topic
#
Topic
#
Topic
#
Topic
#
Topic
#
Topic
#
Topic
#
Topic

## Slide 3: What is an STM32MP13?
Cortex A7 (ARMv7-A) architecture
L1 I & D Caches
Level2 Cache
Arm TrustZone security technology
Arm NEON advanced SIMD
DSP and SIMD extensions
VFPv4 floating-point
DDR controller
Connectivity / Analog Peripherals
Much More!

## Slide 4: Supplied Tools & Motivations
The Bare Metal distribution brings MCU simplicity to MPU performance
It allows (forces) the application to manage the hardware resources with no OS
Provides suitable framework for platform validation SW harness
Tools and Distributions referenced in this slide deck
  HAL_MP13_V1.0.0
    https://www.st.com/en/embedded-software/stm32cubemp13.html
  CubeIDE V 1.13.0
    https://www.st.com/en/development-tools/stm32cubeide.html#
  CubeProgrammer V 2.14.0
    https://www.st.com/en/development-tools/stm32cubeprog.html
  Starter Package for OSTL on MP13DK
    https://www.st.com/en/embedded-software/stm32mp1starter.html#get-software

## Slide 5: Components of the Bare Metal Package
The HAL release for MP13 allows for Bare Metal application creation
The distribution includes
  CMSIS device implementation
    Core related files for the device
  Peripheral Drivers
    Drivers for each of the HW peripherals
  Example Projects
    Small examples for peripheral usage
  Application Projects
    Combine multiple aspects of the HW and SW in single project

## Slide 6: CubeIDE
ST Integrated Development Environment
  Based on Eclipse IDE
  Source Editor
  Build Management
  Debugger
  Code Generation
    Integrated CubeMX
    Linux Device Trees (today)

## Slide 7: CubeProgrammer
ST Utility to ease programming of embedded memory on platforms
Programming
Interface Selection
Programming layout Config File
Visualization of what is to be programmed
Real time feedback on the Programming Process

## Slide 8: Compiling From the Bare Metal Distro

## Slide 9: Let's Build Something
Importing an existing Example Project
  File -> Import -> Existing Projects Into Workspace
Browse to the installed examples for project path
  Use the GPIO_EXTI as an example

## Slide 10: Resulting Project in CubeIDE
New Project exists
Start a Build
Tools Output

## Slide 11: STM32MP13-DK Overview

## Slide 12: STM32MP13-DK
STM32 MP13 Discovery Kit
  STM32MP135F
  512M DDR3 (16 bit)
  2 x Ethernet 100M
  WLAN / Bluetooth
  STLink V3 Embedded
  USB A
  USB C
  CSI Camera Interface
  4.3" LCD Screen
  User Buttons / LEDs
  SDCard Interface

## Slide 13: MP13DK Platform Settings
MICRO-USB jack STLink Debug port
Boot Pin DIP switch
USB-C jack (Power Supply)
Underside of board
ENGINEERING Boot Configuration

## Slide 14: Debugging an Application

## Slide 15: Launch Debug
Once compiled and linked Press the DEBUG button to generate a debug configuration
The defaults are all good but can be modified later from the DEBUG configuration dialog

## Slide 16: To The Debugger
Prompted to switch to the debug interface
Display of Active Threads
Debug command buttons
Current execution source

## Slide 17: Debug Interface
Additional views
  Local variables
  Peripheral Registers
  Breakpoint display
  Memory Windows
  etc

## Slide 18: Is This Thing On?
"Run" the application with the "Play" button
GREEN LED toggles with Button USER1

## Slide 19: Memory Configurations

## Slide 20: Memory Configurations
By Default
  Examples are built for SYSRAM
Let's Look at the output MAP file for the build
code was linked to 0x2FFE0000 (SYSRAM)

## Slide 21: Run from DDR
Compiling for SYSRAM allows for portable example applications
- BUT - what if the application doesn't fit in 128KB
The Platform DDR memory space is also available
  MP13DK platform has 512M memory of DDR
To run from DDR
  Link start of Memory @ 0xC0000000
  Initialize the DDR periph and memory
  Once DDR configured, ensure application
    doesn’t change DDR voltage rails
    doesn’t change DDR clocking

## Slide 22: Link start of Memory @ 0xC0000000
Example application link script is stm32mp13xx_a7_sysram.ld
REGION_ALIAS("RAM", SYSRAM_BASE);
  Let's modify this to be
REGION_ALIAS("RAM", DDR_BASE);
Re-link the Application
  Application now linked @0xC0000000 (DDR)

## Slide 23: Initialize the DDR periph and memory
DDR_Init application example is provided for DDR memory Initialization
  Import an Existing project just like before, but this time for the DDR_Init directory
Rebuild the project with no modifications
Run the project – BLUE LED will start to flash

## Slide 24: Don't change DDR voltage rails or DDR Clocking
Example applications have !defined(USE_DDR) surrounding PMIC and Clock init
  Define this to keep the example app from resetting the DDR config done by DDR_Init
Define USE_DDR for the example application
  ProjectProperties -> … -> Settings

## Slide 25: Modify Debug Configuration
Remove the monitor reset call in the debug startup
  "monitor reset" will lose the DDR configuration previously established by running DDR_Init

## Slide 26: Run From DDR
Full Steps
  Compile DDR_Init and run on board
    BLUE LED flashing
  Modify GPIO_EXTI
    Add USE_DDR to defines
    Change Link Map to DDR_MEM
    Remove "monitor reset" from debug configuration
    Debug the GPIO_EXTI project with same results
      GREEN LED toggles with Button USER1
Awesome! You're Running From DDR

## Slide 27: Boot Capabilities

## Slide 28: Embedded Linux Boot Phases
ROM code
  minimally configures clocks
  Configures boot storage device
  Jumps to First Stage Bootloader
First Stage Bootloader
  Additional clock configuration
  DDR configuration
  Load second stage bootloader (uboot for Linux)
    OR
  Load Bare Metal Application

## Slide 29: Boot Capabilities
If you want the BOOT ROM to load your binary directly from SDCard
  We can use a dedicated FSBL (First Stage Boot Loader)
  ROM code needs specific information about the binary to be loaded
    This is held in the Binary header, created by the signature step in the build
It is also possible to use the OpenSTLinux boot components as the bootloader
  In this case the TF-A and OPTEE binaries would be executed as normal, but the uboot binary would be replaced with the bare metal application

## Slide 30: Dedicated FSBL
A dedicated FSBLA application for SDCard is supplied in the HAL distribution
Directory includes the TSV file for CubeProgrammer to flash the Loader and App

## Slide 31: Sign the Application
In this case "Signing" the application is not about security
  The FSBLA boot loader application needs additional information about the binary it is loading
    Memory address to load the binary to
    Size of Binary
There are scripts included with the HAL distribution to create and prepend this header to the application binary
Add command to the application post build steps in the IDE project properties
  arm-none-eabi-objcopy -O binary "${BuildArtifactFileBaseName}.elf" "${BuildArtifactFileBaseName}.bin" && "../postbuild.sh" "." "${BuildArtifactFileBaseName}.bin" "${BuildArtifactFileBaseName}_Signed.bin" "-bt 10" "-ep C0000000"
Once the build completes the signing, the signed application can be copied to the FSBLA directory

## Slide 32: Sign / Copy

## Slide 33: Prep the SD Card on the Platform
The FSBLA needs to be written to a formatted SDCard
There is a "delete all" TSV file included in the starter package that can be used from CubeProgrammer to delete all partitions on the supplied SDCard

## Slide 34: Flash the Application
The FSBLA and Signed Application can now be written to the Formatted SDCard
The supplied Programming Firmware expectes to be connected Via SERIAL port
  The USB-C cable connected to CN7 MUST be disconnected for the download to work
  Set Boot Pins to all 0 for USB / Serial communication
  Connect & Download

## Slide 35: One Thing Left To Do!
Set boot pins back to Boot from SD
Reset the board (Black Button)
Your application starts!
  Pressing USER1 button toggles Green LED
  Same operation as before
    BUT loaded by the FSBLA from the SD Card

## Slide 36
Find out more at www.st.com
You can personalize this
last page with a short link
(ex. www.st.com/shortlink)
You can find a complete list of st.com short links on this page:
http://seo.st.com/toolbox/shortcuts/